## Slide 1: Big Four Construction Hazards: Fall Hazards
This material was produced under grant number SH-17792-08-60-F-48 Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Revision were made to this material under grant number SH-05022-SH8 from the Occupational Safety and Health Administration, U.S. Department of Labor.

## Slide 2: Hazards

## Slide 3: Building Structures
Work conditions 6’ or more above lower level require the use of fall protection:
  Unprotected sides, edges
  Leading edges
  Excavations
  Walking/working surfaces

## Slide 4: Building Structures
Damaged or missing guardrails must be fixed immediately.

## Slide 5: Hazards

## Slide 6: Scaffolds
Never stack blocks, bricks, or use ladders on top of scaffolds for extra height.

## Slide 7: Scaffolds

## Slide 8: Scaffolds
Workers must have a safe way to access the scaffold.

## Slide 9: Scaffolds
Scaffold bases must rest on a base plate and a mud sill.
Base plate
The base plate is designed to level and support the scaffold.
Mud sill

## Slide 10: Scaffolds
Scaffolds are elevated, temporary work platforms:
  Supported scaffold
  Guardrails
  Access ladders
  Powered work platforms

## Slide 11: Hazards

## Slide 12: Ladders

## Slide 13: Ladders
When using a portable ladder for access to an upper landing surface, the side rails must extend at least 3’ above the upper landing surface.

## Slide 14: Ladders
Ladders must be positioned at a safe angle to avoid potential fall hazards when climbing.
Extension ladders must extend 3’ over the landing for safe access.

## Slide 15: Job Made Ladders
Job made ladders must be properly constructed:
  Steps equally spaced
  No missing steps or rungs
  No sharp edges or
nails sticking out

## Slide 16: Floor Covers

## Slide 17: Floor Covers
Sky-lights are another form of floor holes.
Never sit, stand, or place any materials on sky-lights.

## Slide 18: Floor Covers
The cover must be marked to make sure everyone knows it is a safety device.

## Slide 19: Floor Covers
All floor holes where an employee could fall through must be covered or guarded.